## Slide 1
AutoCAD
ELECTRICAL
COURSE SLIDES · WSQ
Technical Drawing with AutoCAD Electrical
WSQ Course Code: TGS-2023037466
TSC: Technical Drawing · DSN-TDR-4005-1.1
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version 6.0 · 18 August 2026
Trainer: ______________________ · www.tertiarycourses.com.sg · enquiry@tertiaryinfotech.com · +65 6100 0613
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved.

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
1

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
?
Your Trainer
General Trainer template — to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
QUALIFICATIONS
PhD — data science, engineering design and CAD/CAE practice.
DELIVERS
WSQ courses on technical drawing (AutoCAD, AutoCAD Electrical, Revit, Fusion 360) and engineering software.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name and organisation / role.
• Your experience with AutoCAD or electrical design (if any).
• What you want to be able to draw or document after this course.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is stupid.
3
Respect each other's views.
4
Exit silently for calls or toilet breaks.
5
Be punctual; return from breaks on time.
6
75% attendance is required for funding.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 8
COURSE PORTAL · LMS/TMS
Download Course Material
• All course materials live on the Tertiary Infotech LMS/TMS portal.
• Portal: https://lms-tms.tertiaryinfotech.com
• Log in with the credentials sent to your registered email.
• Download the slides and Learner Guide — you may use them during the open-book assessment.
• Your attendance records, assessment submission and certificate are also on the portal.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 9
SCHEDULE · 0930 – 1830 DAILY
Lesson Plan — 2 Days
Day 1
Day 2
• Day 1 — Getting started, projects and schematic drawing
– Digital attendance (AM) · introductions · learning outcomes · course outline
– Topic 1: Introduction to Technical Drawing Using AutoCAD Electrical (Labs 1–2)
– Lunch break · digital attendance (PM)
– Topic 2: Analysing Technical Drawings (Labs 3–4)
– End of Day 1
• Day 2 — Analysis, documentation, submission and assessment
– Digital attendance (AM) · Day 1 recap
– Topic 2 (continued): cross-referencing & review (Lab 5)
– Topic 3: Reviewing Drawings for Strategic Relevance & Standard Compliance (Labs 6–8)
– Course feedback & TRAQOM survey · digital attendance (Assessment)
– Final Assessment: WA (SAQ) 1 hr + PP 1 hr
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 10
WSQ · SKILLS FRAMEWORK
Skills Framework
• TSC Title: Technical Drawing
• TSC Code: DSN-TDR-4005-1.1
• This course is mapped to the Skills Framework for Design — Technical Drawing TSC.
• The assessment covers every Knowledge (K1–K6) and Ability (A1–A6) statement of the TSC.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 11
DSN-TDR-4005-1.1 · KNOWLEDGE (ASSESSED IN THE WA)
TSC Knowledge Statements
1
K1
Symbols, standards and conventions used in technical drawings across various fields and regions
2
K2
Methods of technical drawing by instruments and computer-aided design (CAD) systems
3
K3
Types of technical drawings
4
K4
Technical drawing standards
5
K5
Fundamentals of drafting design documentation
6
K6
Concepts of information technology (IT) to facilitate the usage of technical drawing software
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 12
DSN-TDR-4005-1.1 · ABILITIES (ASSESSED IN THE PP)
TSC Ability Statements
1
A1
Devise metrics and guidelines for the production of technical drawings
2
A2
Formulate solutions for problems encountered during the development of technical drawings
3
A3
Review technical drawings for accuracy and adherence to established specifications
4
A4
Analyse drawings to determine their construction needs to deliver upon design solutions
5
A5
Review technical drawings and/or changes to them, to ensure relevance to the organisation's strategies
6
A6
Review drawings and specifications to ensure conformance to requirements of relevant standards for submission
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 13
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 — Devise & solve
Devise metrics for technical drawing production with AutoCAD Electrical and formulate solutions for development problems. (K1, K2, A1, A2)
2
LO2 — Analyse & review
Analyse technical drawings to determine construction needs while reviewing accuracy and adherence to specifications. (K3, K4, A3, A4)
3
LO3 — Strategy & standards
Review drawings for relevance to the organisation's strategies and conformance to submission standards. (K5, K6, A5, A6)
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 14
THREE LEARNING UNITS · EIGHT HANDS-ON LABS
Course Outline
Topic 1 · Introduction
• AutoCAD Electrical user interface
• Symbols, standards & conventions
• Ribbon, palettes & navigation
• Projects & drawing management
• Labs 1–2
Topic 2 · Analysing Drawings
• Types of schematic drawings
• Components, terminals & PLC symbols
• Wires, numbers & signal arrows
• Cross-referencing & review tools
• Labs 3–5
Topic 3 · Review & Compliance
• Drafting design documentation
• Panel layouts & part-list reports
• Custom symbols
• Plot & publish for submission
• Labs 6–8
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 15
BEFORE THE ASSESSMENT
Briefing for Assessment
• Place phones and other materials under the table or on the floor.
• No photos or recording of assessment scripts.
• No discussion during the assessment.
• Use a black/blue pen for hard-copy assessments.
• No liquid paper / correction tape.
• Scripts are collected when time is up.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 16
FINAL ASSESSMENT · DAY 2
Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 1 hour, open book. (K1–K6)
• Practical Performance (PP) — hands-on AutoCAD Electrical tasks, 1 hour, open book. (A1–A6)
• Format: Open Book — slides, Learner Guide and approved materials only.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
• An appeal process is available if required.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 17
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then PP — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 18
WSQ FUNDING
Criteria for Funding
• Minimum attendance rate of 75% based on the SSG Digital Attendance record.
• Complete the assessment and be assessed as 'Competent'.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 19
TOPIC 01
Introduction to Technical Drawing Using AutoCAD Electrical
User interface · symbols, standards & conventions · ribbon · navigation · projects & drawings (K1, K2 · A1, A2)
01
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 20
MAPS TO LO1
Key Concepts — Topic 1
1
Symbols, standards, conventions
IEEE 315/315A, IEC-60617 and NFPA symbol libraries make an electrical drawing readable across fields and regions. (K1)
2
CAD vs manual drawing
AutoCAD Electrical automates tagging, wire numbering and cross-referencing that instrument drawing does by hand. (K2)
3
The AutoCAD Electrical UI
Ribbon tabs, Quick Access Toolbar, marking menu, palettes, status bar, command line and navigation tools.
4
Projects drive everything
A .wdp project file groups interrelated drawings so project-wide functions can retag, renumber and report.
5
Devise metrics & guidelines
Templates, drawing properties, reference systems and title blocks standardise production. (A1)
6
Formulate solutions
Grid/snap, ortho, object snap and the Circuit Clipboard solve day-to-day drawing development problems. (A2)
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 21
TOPIC 01 · USER INTERFACE · K2
Ribbon Tabs and Panels
• AutoCAD Electrical presents a standard tabbed ribbon across the top of the drawing area.
• Electrical-specific tabs (Schematic, Panel, Reports) sit alongside the core AutoCAD tabs.
• Each tab is divided into panels that group related commands.
• Right-click in the tabs area to choose which tabs and panels to display or hide.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 22
TOPIC 01 · USER INTERFACE · K2
Quick Access Toolbar
• The Quick Access Toolbar keeps New, Open, Save, Plot and Undo one click away.
• It also carries navigation commands used frequently in AutoCAD Electrical.
• Customise it: click the drop-down at its right end and tick the commands you use most.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 23
TOPIC 01 · USER INTERFACE · K2
Marking Menu
• The marking menu is a radial context menu: hover an electrical object and right-click.
• The options shown depend on the type of object under the cursor — click one to run it.
• Power use: press-and-hold right-click, move the cursor toward the desired option, release — a gesture runs the command directly.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 24
TOPIC 01 · USER INTERFACE · K2
Palettes
• Palettes manage projects (Project Manager) and the catalog database (Catalog Browser).
• A palette stays on screen while other commands run — always accessible.
• Dock, resize or set auto-hide to control how much drawing space a palette uses.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 25
TOPIC 01 · DEVISE METRICS · A1
Status Bar — Precision Settings
• The status bar toggles the settings that make a drawing accurate and precise.
• Grid (F7) displays the reference grid; Snap (F9) locks the cursor to grid points.
• Ortho (F8) constrains movement to horizontal/vertical; Polar tracks set angles.
• 2D Object Snap (F3) jumps to endpoints, midpoints and circle centres as you draw.
• These settings are your first production metric: set them before you draw.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 26
TOPIC 01 · DRAWING ENVIRONMENTS · K2
Model Space and Paper Space
• Model space is a limitless drawing area where you draw at 1:1 real-world size.
• First decide what one unit represents (1 mm, 1 cm, 1 inch …) — then draw to that scale.
• Paper space (layouts) arranges scaled views of the model on a titled sheet for plotting.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 27
TOPIC 01 · USER INTERFACE · K2
Command Line
• The Command window accepts commands and system variables and prompts you through each command sequence.
• Every ribbon click has a typed equivalent — experienced drafters mix both.
• Ctrl+9 toggles the command window display.
• Watch the prompts: they tell you exactly what input the command expects next.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 28
TOPIC 01 · VIEW CONTROL · K2
Navigation Tools
• Pan moves the view parallel to the screen; Zoom changes magnification; Orbit rotates 3D views.
• Mouse shortcuts: press the scroll wheel to Pan, roll it to Zoom, double-click it to Zoom Extents.
• ZOOM (Z) options: All shows everything, Window zooms a picked area, Previous restores up to 10 earlier views, Scale magnifies by factor.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 29
TOPIC 01 · PROJECT-BASED CAD · A1
Projects — the .wdp File
• AutoCAD Electrical is project-based: a project is a set of interrelated drawings.
• All project information — including the drawing list — is saved in a .wdp project file.
• Project Manager creates, opens and manages projects and their settings.
• Working project-wide is what lets tags, wire numbers and cross-references stay consistent.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 30
TOPIC 01 · PROJECT-BASED CAD · A1
Project Manager
• Project Manager is a palette — it can stay on screen while you use other commands.
• It can be docked, resized and set to auto-hide.
• Create a project and the .wdp file lands in your chosen folder; the new project becomes active and you add drawings to it.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 31
TOPIC 01 · DEVISE GUIDELINES · A1
Project Properties
• Define library paths, drawing format and reference style when you start a project — or any time later.
• Two kinds of properties: drawing defaults (copied into each new drawing) and project-wide settings.
• Setting properties once at project level is how an organisation standardises its drawings.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 32
TOPIC 01 · PROJECT-BASED CAD
Activate a Project
• Activate from the list of open projects in Project Manager.
• Or browse to the project's .wdp file, or pick from the recent-projects list.
• An opened project joins the Project Manager list and becomes the active project.
• Copy an existing project to reuse its properties, drawings and support files in a new job.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 33
TOPIC 01 · DRAWING MANAGEMENT
Drawings in a Project
• The drawing order sets the processing order for project-wide functions — drag and drop to reorder.
• Add folders within a project to organise drawings.
• New Drawing creates a drawing inside the active project; give it a template with predefined electrical properties, wire layers, a reference system and a title block.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 34
TOPIC 01 · DEVISE METRICS · A1
Drawing Properties
• Drawing Properties control tagging and referencing per sheet: sheet values, installation and location codes.
• Reference system: ladder, X-Y Grid or X Zones; formats for component tags, wire numbers and cross-references.
• Styles: PLC modules, wire crossing and wire connection appearance.
• Properties come from the template or the project defaults — override via OK-Properties when creating the drawing.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 35
TOPIC 01 · REUSE · A2
Copy and Add Drawings
• Copy a single drawing from any open project into the active project via Project Manager.
• Add existing drawings any time — the way to reuse sheets from a previous job.
• After adding, run Project-Wide Update/Retag to refresh ladder references, component tags, wire numbers and cross-references.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 36
TOPIC 01 · DRAWING MANAGEMENT
Reference-Only Drawings
• Some drawings belong to the project but must not be processed by project-wide functions.
• Mark them Reference Only in the drawing properties — tagging, cross-referencing and reporting skip them.
• Typical examples: cover sheets, general notes, mechanical outlines.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 37
TOPIC 01 · STANDARDS · K1
Title Block Setup
• Insert a .dwg as the title block and link project/drawing property values to its attributes.
• Title Block Setup creates and defines the mapping between properties and attributes.
• Once mapped, sheet number, description and revision fill in automatically on every sheet — a core drafting standard.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 38
TOPIC 01 · STANDARDS · K1 K4
Reference Systems — Ladders, X-Y Grid, X Zones
• Each schematic drawing can define a reference system: ladder rungs, X-Y grid or X zones.
• The reference system assigns unique component tags and wire numbers (unless sequential tagging is used).
• It also drives cross-referencing between parents and children.
• Insert the ladder or grid from Schematic → Insert Wires/Wire Numbers; define it on a template to save time.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 39
WHAT YOU'LL DO
Hands-On Labs — Topic 1
Lab 1
• Set Up a New AutoCAD Electrical Drawing
• A correctly configured metric drawing sheet, saved as a reusable baseline for the rest of the course.
Lab 2
• Create a Project with Project Manager
• A working .wdp project containing the supplied power and lighting plan drawings plus a title block, in the correct sheet order.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 40
TOPIC 01 · HANDS-ON
Set Up a New AutoCAD Electrical Drawing
LAB 1
Create a new drawing from the ACADISO template, then set the workspace, drawing limits and units — the production metrics every drawing in your organisation should start from.
You'll build
A correctly configured metric drawing sheet, saved as a reusable baseline for the rest of the course.
Tools: AutoCAD Electrical · ACADISO template · Status bar · Grid & Snap
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 41
LAB 1 · STEP BY STEP
Set Up a New AutoCAD Electrical Drawing
1
Start AutoCAD Electrical and create a new drawing from the ACADISO template (New → acadiso.dwt).
NEW → acadiso.dwt
2
Set the Electrical workspace from the Workspace Switching control on the status bar.
WSCURRENT → Electrical
3
Set the drawing limits to an A3 metric sheet (0,0 to 420,297) and Zoom All to see the full sheet.
LIMITS 0,0 420,297 then ZOOM All
4
Set the units to decimal millimetres with 0 precision (Format → Units).
UNITS → Decimal · 0
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 42
LAB 1 · STEP BY STEP
Set Up a New AutoCAD Electrical Drawing
5
Turn on Grid (F7) and Snap (F9) from the status bar and open DraftingSettings.dwg to compare a pre-configured sheet.
GRID 10 · SNAP 10
6
Save the drawing as MyBaseline.dwg — this is your production guideline drawing.
SAVEAS MyBaseline.dwg
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 43
LAB 1 · VERIFY
Set Up a New AutoCAD Electrical Drawing
✅ Test it
ZOOM All shows the full 420×297 sheet, the crosshair snaps in 10 mm increments, and STATUS reports decimal units — your baseline metrics are in force.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 44
TOPIC 01 · HANDS-ON
Create a Project with Project Manager
LAB 2
AutoCAD Electrical is project-based: a .wdp project groups interrelated drawings so project-wide functions can retag and renumber. Create a project, add the supplied electrical plan drawings, and reorder them.
You'll build
A working .wdp project containing the supplied power and lighting plan drawings plus a title block, in the correct sheet order.
Tools: Project Manager · .wdp project file · Power_Plan / Lighting_Plan DWGs
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 45
LAB 2 · STEP BY STEP
Create a Project with Project Manager
1
Open Project Manager from the Project tab (it is a palette — dock it on the left).
AEPROJECT
2
Create a new project named TRAINING — the .wdp file stores the project description and settings.
Project Manager → New Project → TRAINING
3
Review the Project Properties: library standard (IEC/IEEE/NFPA), component tag format and cross-reference style.
Right-click project → Properties
4
Add the supplied drawings 10-2_Power_Plan.dwg and 10-2_Lighting_Plan.dwg to the project.
Right-click project → Add Drawings
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 46
LAB 2 · STEP BY STEP
Create a Project with Project Manager
5
Drag and drop the drawings inside Project Manager so the power plan is sheet 1, and add Title_Block.dwg as reference-only.
Drag to reorder · Properties → Reference Only
6
Make TRAINING the active project and open a drawing from the project list by double-clicking it.
Right-click → Activate
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 47
LAB 2 · VERIFY
Create a Project with Project Manager
✅ Test it
Project Manager shows TRAINING in bold (active) with the drawings in your chosen order, and the .wdp file exists in the project folder — project-wide functions now see every sheet.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 48
TOPIC RECAP
Recap — Topic 1
• A1 — devise metrics and guidelines for technical drawing production (template, workspace, limits, units) (Lab 1)
• A1, A2 — standardise production with a project; solve multi-drawing organisation problems (Lab 2)
• Key concepts: Symbols, standards, conventions, CAD vs manual drawing, The AutoCAD Electrical UI, Projects drive everything, Devise metrics & guidelines, Formulate solutions.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 49
Lunch Break
Back at 1245 · PM digital attendance

## Slide 50
TOPIC 02
Analysing Technical Drawings
Types of schematic drawings · components, terminals & PLC symbols · wires & part lists · accuracy review (K3, K4 · A3, A4)
02
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 51
MAPS TO LO2
Key Concepts — Topic 2
1
Types of technical drawings
Schematics, panel layouts, wiring diagrams, one-line diagrams and reference-only sheets each serve a construction purpose. (K3)
2
Technical drawing standards
Ladder references, X-Y grids, wire-number formats and cross-reference styles are the standards drawings are checked against. (K4)
3
Schematic components
Insert from the icon menu or catalog database; annotate with tags, descriptions and catalog data.
4
Terminals & PLC symbols
Standard part lists rely on terminal strips and parametric PLC I/O modules that adapt to the ladder.
5
Wires, numbers & arrows
Wire layers, wire numbers and source/destination signal arrows carry the circuit across sheets.
6
Review for accuracy
Cross-referencing, Surfer and Mark/Verify audit a drawing set for accuracy and adherence to specifications. (A3, A4)
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 52
TOPIC 02 · DRAWING TYPES · K3
Types of Technical Drawings
• Schematic diagrams show circuit logic: ladders, components, wires and signals.
• Panel layout drawings show the physical arrangement of components in an enclosure.
• Wiring / connection diagrams document point-to-point conductor runs and terminal strips.
• One-line (single-line) diagrams summarise power distribution at system level.
• Reference-only sheets (covers, notes, outlines) support the set without carrying circuit data.
• Each type answers a different construction need — a full drawing set uses them together.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 53
TOPIC 02 · SCHEMATICS · K4
Schematic Components — Grid and Snap Discipline
• Insert schematic components, generate PLC modules, and insert or copy circuits.
• Work with grid lines on and snap-to-grid when inserting components.
• GRID sets grid spacing; SNAP sets snap spacing; F7 toggles grid visibility, F9 toggles snap.
• Consistent snap spacing keeps rungs aligned so wires connect cleanly — an accuracy standard.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 54
TOPIC 02 · STANDARDS · K1
Symbol Library Standards
• AutoCAD Electrical ships symbol libraries complying with IEEE 315/315A, IEC-60617 and NFPA.
• IEEE and IEC libraries are metric; NFPA library symbols are in inches (scale with the Modify-library utility).
• The old JIC standard was absorbed into NFPA 79; JIC and older IEC libraries remain for legacy support.
• Pick ONE standard per project in Project Properties — mixing standards breaks readability across regions.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 55
TOPIC 02 · COMPONENTS
Insert a Component from the Catalog Database
• Know the part number already? Insert the component straight from the catalog database.
• Use the Catalog Browser palette; search values are saved for quick reuse.
• Catalog information lands on the symbol automatically; edit further in the Insert/Edit dialog that follows insertion.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 56
TOPIC 02 · COMPONENTS
Insert a Component from the Icon Menu
• The icon menu inserts by symbol type — a NO push button, a 3-position selector switch, and so on.
• Different icon menus exist per library set; choose the project's icon menu under Project Settings.
• After insertion, annotate with descriptions and catalog information.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 57
TOPIC 02 · COMPONENT DATA · A3
Annotate the Symbol
• Each symbol carries a main catalog value plus optional multiple-catalog values.
• Edit a component to add, change or remove catalog assignments — Lookup opens the catalog search.
• Multiple Catalog attaches auxiliary parts (contact blocks, adapters) to the same device.
• Complete, accurate annotation is what makes reports and BOMs trustworthy downstream.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 58
TOPIC 02 · COMPONENT MODEL · K4
Parent and Child Components
• Some devices are drawn as several symbols — a relay is a coil plus its contact symbols.
• The coil is the parent; contacts are children that inherit its tag and data.
• When inserting a child, pick its parent from the active drawing or project list in the Insert/Edit Child dialog.
• Parent/child links power the cross-reference grid you will read in every review.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 59
TOPIC 02 · PLC SYMBOLS · K3
PLC I/O Modules
• AutoCAD Electrical generates hundreds of PLC I/O modules on demand, in multiple graphical styles.
• Modules adapt automatically to the underlying ladder rung spacing.
• Expand manufacturer → series → type, pick the module and style, then place it by insertion point.
• Parametric generation keeps PLC drawings consistent with the wiring standard in force.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 60
TOPIC 02 · REUSE · A4
Circuits and Circuit Builder
• A circuit is any collection of components and wires; save frequently used circuits to the icon menu.
• A saved circuit re-inserts with tags updating automatically to stay unique.
• Circuit Builder assembles motor-control and power-feed circuits dynamically from your dialog selections.
• Building from proven circuits is how construction needs are met quickly and correctly.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 61
TOPIC 02 · TERMINALS · K3
Schematic Terminals
• Insert terminals like other schematic symbols — from the Catalog Browser (TRMS category) or the icon menu.
• Four terminal behaviour types exist; the terminal block name controls the behaviour.
• Pick the behaviour type and terminal style carefully when inserting from the icon menu.
• The TERMINAL STRIP command inserts strip symbols using Installation, Location and Tagstrip values.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 62
TOPIC 02 · TERMINALS
Terminal Block Properties
• A schematic terminal symbol represents a single-level terminal or ONE level of a multi-level terminal.
• The number of levels is a block property; each level carries its own wiring data.
• View and edit properties in the Insert/Edit Terminal Symbol dialog.
• Associate schematic terminals across levels — and manage whole strips in the Terminal Strip Editor.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 63
TOPIC 02 · WIRING · K4
Wires and Wire Layers
• A wire is a line object on a layer defined as a wire layer; a wire network is connected wire segments.
• Manage wire layers in a grid: edit colour and size inline, right-click to rename.
• Create layers for wire families (24VDC, 230VAC, earth) so wiring intent is visible at a glance.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 64
TOPIC 02 · WIRING
Insert Wires
• Inserted wires land on a wire layer automatically — joining an existing wire adopts that wire's layer.
• A tee connection receives a dot or angled tee per the Styles tab of Drawing Properties.
• Change/Convert Wire Type moves wires to another layer or converts plain lines into wires.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 65
TOPIC 02 · STANDARDS · K4
Wire Number Setup
• The Wire Numbers tab of Drawing Properties defines the wire-number format, type and placement.
• The format mixes text and replaceable parameters: %N (number), %S (sheet), %D (drawing), %X (suffix position), %P/%I/%L (IEC project / installation / location codes).
• Wire numbering is a specification — every sheet in the set must follow the same format.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 66
TOPIC 02 · WIRING · A3
Insert Wire Numbers
• The Wire Numbers command inserts new numbers or updates existing ones drawing- or project-wide.
• Drawing-property settings are preselected; override per run if needed.
• Numbers marked Fixed are preserved by renumbering — edit them via Edit Wire Number.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 67
TOPIC 02 · MULTI-SHEET WIRING
Signal Arrows
• A signal arrow breaks a wire network and continues it elsewhere — same drawing or another sheet.
• AutoCAD Electrical uses named source/destination pairs: give the source a code, then insert destinations that reference it.
• Arrows carry cross-reference annotation both ways, so a checker can trace the signal across the set.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 68
TOPIC 02 · REVIEW FOR ACCURACY · A3
Cross-Referencing
• Cross-references annotate related components with each other's reference locations.
• Three annotation styles on a parent; child annotation is always text format.
• Signal arrows are cross-referenced too — source shows destinations, destination shows its source.
• Set the format and style on Drawing Properties → Cross-References; keep it current before any review or PDF publish.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 69
TOPIC 02 · REVIEW FOR ACCURACY · A3
Surfing Between Components
• Surfer jumps between related components and follows signal arrows across drawings.
• Pick a parent and surf to each child, or follow a source arrow to its destinations.
• Surfing is the fastest way to audit that parents, children and signals all agree.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 70
TOPIC 02 · MODIFY · A2
Modify Commands — Edit Without Breaking Intelligence
• Always modify with the Electrical editing commands so component intelligence survives.
• Align components; Move — tags update, wires heal and break as needed.
• Copy with multiple insertion points — tags stay unique; optionally update terminal numbers.
• Circuit Clipboard (Cut/Copy/Paste) moves components and wires between drawings.
• Quick edits: delete-and-heal, toggle NO/NC contact state, swap a block.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 71
TOPIC 02 · REUSE AT SCALE · A4
Project-Wide Updates
• Reusing drawings from a previous design? Update the reference system, retag components, reassign wire numbers and refresh cross-references in ONE pass.
• Project-Wide Update/Retag runs across every non-reference drawing in the project.
• This is what keeps a copied design consistent instead of quietly wrong.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 72
TOPIC 02 · CHANGE CONTROL · A3
Track Changes — Mark and Verify
• Mark/Verify tracks changes to your drawings — even changes made outside AutoCAD Electrical.
• Mark records the current state before edits begin.
• Verify afterwards reports every change — print it or surf straight to each changed object.
• A marked-and-verified set gives the reviewer an exact change list to check against the specification.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 73
WHAT YOU'LL DO
Hands-On Labs — Topic 2
Lab 3
• Build Circuits with Circuit Builder
• A schematic sheet containing a Circuit Builder motor circuit plus a saved, reusable circuit block.
Lab 4
• Insert Wires, Wire Numbers and Terminals
• A correctly wired and wire-numbered circuit with terminals, matching the drawing's wire-number specification.
Lab 5
• Cross-Reference and Surf a Drawing Set
• A cross-referenced two-sheet circuit you can navigate with Surfer, plus a Mark/Verify change report.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 74
TOPIC 02 · HANDS-ON
Build Circuits with Circuit Builder
LAB 3
Use Circuit Builder to insert a three-phase motor-control circuit built dynamically from your selections, then save a frequently used circuit and re-insert it from the icon menu.
You'll build
A schematic sheet containing a Circuit Builder motor circuit plus a saved, reusable circuit block.
Tools: Circuit Builder · Icon Menu · Schematic components · Saved circuits
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 75
LAB 3 · STEP BY STEP
Build Circuits with Circuit Builder
1
Open the supplied blank sheet 2-0_Blank.dwg inside your TRAINING project and insert a ladder to carry the circuit.
AELADDER
2
Launch Circuit Builder from the Schematic tab and pick a 3-phase motor circuit from the tree.
AECIRCBUILDER
3
Step through the Circuit Configuration dialog — select the disconnect, protection and control options; the circuit is built dynamically from your selections.
Circuit Builder → Configure → Insert
4
Insert a push button and a selector switch from the Icon Menu to complete the control rung.
AECOMPONENT (Icon Menu)
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 76
LAB 3 · STEP BY STEP
Build Circuits with Circuit Builder
5
Select the finished circuit and save it with Save Circuit to Icon Menu for reuse.
Schematic → Circuit Clipboard → Save Circuit
6
Insert the saved circuit onto a clear area of the sheet and watch tags update to stay unique.
Icon Menu → Saved Circuits
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 77
LAB 3 · VERIFY
Build Circuits with Circuit Builder
✅ Test it
The motor circuit sits on the ladder with unique component tags (M1, PB1 …), and your saved circuit re-inserts with automatically retagged components — construction needs are met without redrawing.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 78
TOPIC 02 · HANDS-ON
Insert Wires, Wire Numbers and Terminals
LAB 4
Insert wires between components, trim them, add automatic wire numbers in the drawing's specified format, and place schematic terminals — the accuracy checks every wiring diagram must pass.
You'll build
A correctly wired and wire-numbered circuit with terminals, matching the drawing's wire-number specification.
Tools: Wires · Wire Numbers · Trim Wire · Schematic Terminals · Power Plan DWG
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 79
LAB 4 · STEP BY STEP
Insert Wires, Wire Numbers and Terminals
1
Continue on your Lab 3 sheet (keep 10-2_Power_Plan.dwg open as an analysis reference for wiring practice).
OPEN 10-2_Power_Plan.dwg
2
Insert two vertical wires between two horizontal rungs — wires land on the wire layer automatically and tee-dots appear at junctions.
AEWIRE
3
Trim the surplus wire segment with Trim Wire (the connected wires heal).
AETRIM
4
Check the wire-number format on the Drawing Properties → Wire Numbers tab (this is the specification you are wiring to).
AEPROPERTIES → Wire Numbers
STEPS 1–4 OF 7
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 80
LAB 4 · STEP BY STEP
Insert Wires, Wire Numbers and Terminals
5
Insert wire numbers project-wide and note that fixed wire numbers are skipped.
AEWIRENO
6
Insert two schematic terminals from the Icon Menu (TRMS category) where the wires leave the sheet.
AECOMPONENT → Terminals
7
Edit one wire number manually and mark it Fixed, then re-run wire numbering to confirm it is preserved.
AEEDITWIRENO
STEPS 5–7 OF 7
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 81
LAB 4 · VERIFY
Insert Wires, Wire Numbers and Terminals
✅ Test it
Every wire carries a number in the drawing-property format, the fixed number survives a project-wide renumber, and the terminals join the wires cleanly — the sheet passes an accuracy review.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 82
TOPIC 02 · HANDS-ON
Cross-Reference and Surf a Drawing Set
LAB 5
Link a parent coil to its child contacts, break a wire across sheets with source/destination signal arrows, then audit the set with Surfer and Mark/Verify — how a checker reviews a real drawing set.
You'll build
A cross-referenced two-sheet circuit you can navigate with Surfer, plus a Mark/Verify change report.
Tools: Cross-referencing · Signal Arrows · Surfer · Mark/Verify · Reference DWG
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 83
LAB 5 · STEP BY STEP
Cross-Reference and Surf a Drawing Set
1
Insert a relay coil (parent) on sheet 1 and a NO contact (child) on sheet 2 of your project; assign the child to the parent in the Insert/Edit Child dialog.
AECOMPONENT → coil / contact
2
Update cross-references and read the parent's contact grid — it reports where every child lives.
AEXREF
3
Break a wire network across the two sheets with a Source arrow (assign a code) and a matching Destination arrow.
AESOURCE · AEDEST
4
Right-click the coil and Surf: jump between the parent, children and signal arrows from the Surf list.
AESURF
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 84
LAB 5 · STEP BY STEP
Cross-Reference and Surf a Drawing Set
5
Mark the project (Mark/Verify), move one component, then run Verify to get the change report.
AEMARKVERIFY
6
Open the supplied reference drawings and identify which sheets are reference-only in Project Manager.
OPEN 10-1_Working_with_References.dwg
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 85
LAB 5 · VERIFY
Cross-Reference and Surf a Drawing Set
✅ Test it
Surfer jumps coil → contact → signal arrow across sheets without manual searching, and the Verify report lists exactly the one component you moved — the set is auditable for accuracy.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 86
TOPIC RECAP
Recap — Topic 2
• A4 — analyse drawings to determine construction needs; assemble standard motor-control circuits (Lab 3)
• A3 — review drawings for accuracy; wire the circuit and number it to specification (Lab 4)
• A3, A4 — review a multi-sheet set for accuracy with cross-references, Surfer and signal arrows (Lab 5)
• Key concepts: Types of technical drawings, Technical drawing standards, Schematic components, Terminals & PLC symbols, Wires, numbers & arrows, Review for accuracy.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 87
SEE YOU TOMORROW · 0930
End of Day 1
Day 2 continues with drawing-set review, documentation, submission — and the final assessment.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 88
Day 2
Digital attendance (AM) · Day 1 recap

## Slide 89
TOPIC 03
Reviewing Technical Drawings for Strategic Relevance and Standard Compliance
Drafting documentation · panel layouts · reports & part lists · custom symbols · plot & publish for submission (K5, K6 · A5, A6)
03
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 90
MAPS TO LO3
Key Concepts — Topic 3
1
Fundamentals of documentation
Panel layouts, nameplates, item numbers and balloons turn a schematic into build documentation. (K5)
2
Reports & part lists
BOM, wire from/to and component reports extract project data for checking and procurement.
3
Custom symbols
Symbol Builder creates house-standard symbols so drawings match the organisation's conventions. (K6)
4
Strategic relevance
Reuse projects, track changes and align drawing sets with the organisation's design strategies. (A5)
5
Standard compliance
Title blocks, xrefs and plot standards keep sheets conformant to submission requirements. (A6)
6
Plot & publish
Output the project to a printer or a hyperlinked multi-sheet PDF for stakeholder submission.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 91
TOPIC 03 · DOCUMENTATION · K5
Fundamentals of Drafting Design Documentation
• A schematic alone cannot be built: documentation adds the physical and procurement views.
• Panel layouts show where each device mounts; nameplates label them; item numbers and balloons key parts to the BOM.
• Reports extract part lists, wire lists and terminal plans from the same project data — no retyping.
• Documentation must align with the organisation's strategies (house symbols, formats) and submission standards. (A5, A6)
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 92
TOPIC 03 · DOCUMENTATION · K5
Panel Layouts
• Insert panel footprint symbols from the schematic component list or the panel icon menu.
• The PANEL ribbon tab carries the layout tools; drawing properties hold panel-specific settings.
• Add components and connect with the insert tools; nameplates, item numbers and balloons complete the layout.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 93
TOPIC 03 · SCHEMATIC → PANEL
Insert Footprints from the Schematic List
• Draw schematics first, then build the panel by selecting from the schematic component list.
• The catalog assignment finds the correct footprint; browse or draw one on the fly if missing.
• The dialog shows which components are already placed; all values copy from schematic to footprint.
• Change a value on either side later and the other side updates — schematic and panel stay consistent.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 94
TOPIC 03 · DOCUMENTATION
Panel Icon Menu and Nameplates
• Components not on the schematic (wire duct, rails) insert from the Panel Icon Menu.
• Insert nameplates from the icon menu and associate each with a footprint.
• Tag, installation, location and descriptions copy from the footprint — override if required.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 95
TOPIC 03 · BOM KEYING · K5
Item Numbers and Balloons
• Item numbers key parts to the BOM; components sharing a catalog value share an item number.
• Panel components are numbered first, then schematic components.
• Set the item-numbering project properties before resequencing.
• Insert balloons to make item numbers visible; multi-catalog components prompt for which value to balloon.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 96
TOPIC 03 · TERMINAL PLANS
Terminal Strip Editor
• Manage an entire terminal strip at once: catalog values, connected components, wires and numbers.
• Resequence terminal numbers, reorder terminals, add spares and accessories, insert jumpers.
• The strip list merges panel terminals and schematic terminals into one editable view.
• Insert the strip graphically — or generate tabular terminal strips with the Table Generator.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 97
TOPIC 03 · PART LISTS · K5
Reports
• Generate project reports: Bill of Material, component lists, wire from/to, terminal plans and more.
• The REPORT command builds custom reports from drawing data; select the report, options and drawings to process.
• Output to a file for procurement, or insert on the drawing as a table for the construction set.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 98
TOPIC 03 · HOUSE STANDARDS · A5
Report Fields and Format Files
• After running a report, include/exclude fields, reorder them and rename labels.
• Save the settings as a .SET format file — unlimited format files per report type.
• Format files ARE the organisation's reporting standard: everyone reproduces the same layout in one click.
• Automatic Reports runs a whole group of formatted reports in a single pass.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 99
TOPIC 03 · PART LISTS
Output a Report — File or Drawing Table
• Save to File exports the report (CSV, XLS, MDB) for procurement and checking.
• Put on Drawing inserts the report as an AutoCAD table — style it with TABLESTYLE.
• The drawing table and the exported file come from the same data, so they cannot disagree.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 100
TOPIC 03 · IT CONCEPTS · K6
Custom Symbols with Symbol Builder
• Symbol Builder creates custom symbols fully compatible with AutoCAD Electrical.
• Start from scratch or from a similar existing symbol; set symbol type, insertion point and orientation.
• For schematic symbols create both the parent and child versions.
• Draw the graphics, then save following the AutoCAD Electrical symbol naming convention — that is what makes the symbol intelligent.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 101
TOPIC 03 · COMPOSITION · K6
External References (Xrefs)
• An external reference attaches another file into the current drawing without copying it.
• The External References palette organises DWG, DWF, DGN, PDF and image references.
• Attach via the palette (View tab → Palettes) or the XREF command; pick the file and placement.
• Xrefs keep shared content (title blocks, outlines) in ONE file — edit once, update everywhere.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 102
TOPIC 03 · SUBMISSION · A6
Plot a Project
• Print an entire project, a subset of sheets, or a single drawing.
• Use Publish/Plot on Project Manager → Plot Project, then pick the drawings to output.
• Select the layout to plot per drawing; use a named page setup for consistent output.
• Map a plot date/time attribute in the title block — it stamps automatically at plot time.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 103
TOPIC 03 · SUBMISSION · A6
Publish to a Hyperlinked PDF
• Publish the project to a multi-sheet PDF that preserves relationships as hyperlinks.
• Tick Multi-sheet file and Include Hyperlinks; the zoom factor sets how close a clicked link zooms.
• Each object carries one hyperlink — reach a child through the parent's cross-reference text.
• Update cross-referencing BEFORE publishing; then reviewers can navigate the set without AutoCAD.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 104
WHAT YOU'LL DO
Hands-On Labs — Topic 3
Lab 6
• Create a Panel Layout with Footprints
• A panel layout drawing with footprints placed from the schematic list, a nameplate, item numbers and balloons.
Lab 7
• Generate Reports and Part Lists
• A BOM table placed on the drawing plus a saved .SET format file and a CSV export of the report.
Lab 8
• Plot and Publish the Project to PDF
• An A3 PDF plot of one sheet and a hyperlinked multi-sheet PDF of the whole project.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 105
TOPIC 03 · HANDS-ON
Create a Panel Layout with Footprints
LAB 6
Generate a panel layout from the schematic component list, insert footprints and a nameplate, and assign item numbers with balloons — drafting design documentation the workshop can build from.
You'll build
A panel layout drawing with footprints placed from the schematic list, a nameplate, item numbers and balloons.
Tools: Panel tab · Schematic List · Footprints · Nameplates · Item balloons · Blocks DWGs
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 106
LAB 6 · STEP BY STEP
Create a Panel Layout with Footprints
1
Create a new panel drawing in your project and switch to the Panel tab of the ribbon.
New Drawing → Panel tab
2
Insert footprints from the schematic list — AutoCAD Electrical matches each component's catalog value to a footprint.
AEFOOTPRINT (Schematic List)
3
Place the footprints inside the panel outline; values (tag, location, description) copy over from the schematic.
Pick insertion points
4
Insert a nameplate from the Panel icon menu and associate it with a footprint.
Panel Icon Menu → Nameplate
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 107
LAB 6 · STEP BY STEP
Create a Panel Layout with Footprints
5
Assign item numbers project-wide — components with the same catalog value receive the same item number.
AEPANELITEM
6
Add item balloons to the footprints and study the supplied blocks/attributes drawings to see how footprint blocks carry data.
AEBALLOON
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 108
LAB 6 · VERIFY
Create a Panel Layout with Footprints
✅ Test it
Each footprint shows the same tag as its schematic parent, the nameplate carries the footprint's description, and balloons display consistent item numbers — the panel documents the design faithfully.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 109
TOPIC 03 · HANDS-ON
Generate Reports and Part Lists
LAB 7
Run Bill of Material and Wire From/To reports across the project, tailor the fields, save a format file for repeat use, and insert the report as a table on the drawing — the part lists a checker reviews.
You'll build
A BOM table placed on the drawing plus a saved .SET format file and a CSV export of the report.
Tools: Reports · Bill of Material · Format files (.SET) · Tables · Attributes DWG
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 110
LAB 7 · STEP BY STEP
Generate Reports and Part Lists
1
Run the Reports tool on the Reports tab and choose Bill of Material, processing the whole project.
AEAUDIT → Reports → BOM
2
Adjust the report: include/exclude fields, reorder columns and rename field labels to your house standard.
Change Report Fields
3
Save the settings as a format file so the same report can be re-run in one click next time.
Save Format File (.SET)
4
Insert the report on the drawing as a table (Put on Drawing) using a table style.
Put on Drawing · TABLESTYLE
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 111
LAB 7 · STEP BY STEP
Generate Reports and Part Lists
5
Export the same report to a file for procurement (CSV/XLS).
Save to File → CSV
6
Run a Wire From/To report and compare it against the wiring you created in Lab 4; open the supplied table drawings to see linked tables.
Reports → Wire From/To
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 112
LAB 7 · VERIFY
Generate Reports and Part Lists
✅ Test it
The BOM table on the drawing matches the CSV export line for line, and re-running the report through your .SET format file reproduces the same layout — the part list is standard-compliant and repeatable.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 113
TOPIC 03 · HANDS-ON
Plot and Publish the Project to PDF
LAB 8
Attach an external reference, then plot a drawing to an A3 PDF and publish the whole project to a single multi-sheet PDF with hyperlinks — the final conformance step before submission.
You'll build
An A3 PDF plot of one sheet and a hyperlinked multi-sheet PDF of the whole project.
Tools: External References · Plot · Publish · Multi-sheet PDF · Layout tabs DWG
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 114
LAB 8 · STEP BY STEP
Plot and Publish the Project to PDF
1
Open the External References palette and attach a DWG as an xref to see how reference files are managed.
XREF → Attach DWG
2
Open 1-12_Using_Layout_Tabs.dwg and review its layout tabs — plotting always happens from a layout with a page setup.
OPEN → Layout tabs
3
Plot the active drawing to PDF at A3 size from the Plot dialog (printer: AutoCAD PDF, paper: ISO A3).
PLOT → AutoCAD PDF → ISO A3
4
From Project Manager, choose Publish/Plot → Plot Project and select the sheets to output.
Project Manager → Plot Project
STEPS 1–4 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 115
LAB 8 · STEP BY STEP
Plot and Publish the Project to PDF
5
Publish the project to a single multi-sheet PDF with Include Hyperlinks checked — cross-references become clickable links.
AEPUBLISH → Multi-sheet · Hyperlinks
6
Open the PDF and click a parent's cross-reference to jump to its child; confirm the title block shows the plot date.
Verify in PDF viewer
STEPS 5–6 OF 6
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 116
LAB 8 · VERIFY
Plot and Publish the Project to PDF
✅ Test it
The A3 PDF matches the layout exactly, and in the multi-sheet PDF clicking a cross-reference hyperlink jumps to the referenced component — the set is ready for standards-conformant submission.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 117
TOPIC RECAP
Recap — Topic 3
• A5 — turn the schematic into build documentation aligned with the organisation's design strategy (Lab 6)
• A6, K5 — extract BOM and wire lists, format them to house standards and place them on the drawing (Lab 7)
• A6 — output the drawing set to submission standards (A3 sheets, hyperlinked multi-sheet PDF) (Lab 8)
• Key concepts: Fundamentals of documentation, Reports & part lists, Custom symbols, Strategic relevance, Standard compliance, Plot & publish.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 118
WRAP-UP
Course Summary & Assessment
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 119
LEARNING OUTCOMES DELIVERED
What You Achieved
1
Set up to standard
Configured drawings from templates with limits, units, grid and snap — production metrics in force. (A1)
2
Projects & drawings
Built .wdp projects, managed drawing order, properties and reference-only sheets. (A1, A2)
3
Schematic drawing
Inserted components, circuits, terminals and PLC modules to IEC/IEEE/NFPA standards. (K1, K3)
4
Wired & numbered
Wired circuits with layered wires, spec-format wire numbers and signal arrows. (K4, A3)
5
Reviewed drawing sets
Audited accuracy with cross-references, Surfer and Mark/Verify. (A3, A4)
6
Documented & submitted
Produced panel layouts, BOM reports, custom symbols and hyperlinked PDF submissions. (K5, K6, A5, A6)
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 120
TEST YOURSELF
Practice Exam
• Sharpen your readiness with the Tertiary Infotech practice exam portal.
• Practice exams: https://exams.tertiaryinfotech.com/
• Attempt it under timed conditions and review every explanation.
• Revisit any lab whose topic you miss, then re-attempt.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 121
CONTINUE YOUR LEARNING · TERTIARYCOURSES.COM.SG
Recommended Courses
1
WSQ - Technical Drawing with AutoCAD
2
WSQ - Technical Drawing with AutoCAD Mechanical
3
WSQ - Application of BIM using Revit
4
WSQ - Architecture Drawing with Revit
5
WSQ - Product Design with Fusion 360
6
WSQ - AutoCAD Civil 3D for Infrastructure Design
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 122
WE'RE HERE TO HELP
Support
• If you have any enquiries during and after the class, contact us:
• Email: enquiry@tertiaryinfotech.com
• Tel: +65 6100 0613
• Website: www.tertiarycourses.com.sg
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 123
FEEDBACK · TRAQOM
Cert & TRAQOM Survey (Mandatory)
• Complete the course feedback and the mandatory SSG TRAQOM survey.
• Your e-certificate is issued via the LMS/TMS portal: https://lms-tms.tertiaryinfotech.com
• The trainer will display the TRAQOM QR code — please complete it before the assessment.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 124
FINAL ASSESSMENT
Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 1 hour, open book. (K1–K6)
• Practical Performance (PP) — hands-on AutoCAD Electrical tasks, 1 hour, open book. (A1–A6)
• Format: Open Book — slides, Learner Guide and approved materials only.
• Submit your completed scripts to the assessor and sign the Assessment Summary Record.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 125
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then PP — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 126
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 127
HAPPY DRAFTING
Thank You!
You are now ready to produce, analyse and review technical drawings with AutoCAD Electrical.
Technical Drawing with AutoCAD Electrical · TGS-2023037466
© 2026 Tertiary Infotech Academy Pte Ltd
126